## Slide 1: RAM TYPES
د. رائد رافع عمر النعمة

## Slide 2: There are two main types of RAM:
There are two main types of RAM:
1- Dynamic Random Access Memory (DRAM): it “loses its stored information in a very short time (for milli sec.) even when power supply is on. D-RAM’s are cheaper & lower.
Similar to a microprocessor chip is an Integrated Circuit (IC) made of millions of transistors and capacitors.” [1]
“Th[e] refresh operation is where dynamic RAM gets its name. Dynamic RAM has to be dynamically refreshed all of the time or it forgets what it is holding. The downside of all of this refreshing is that it takes time and slows down the memory.” [1]
2- Static Random Access Memory (SRAM): it “uses a completely different technology. S-RAM retains stored information only as long as the power supply is on. Static RAM’s are costlier and consume more power. They have higher speed than D-RAMs.” [1]
“Static RAM is fast and expensive, and dynamic RAM is less expensive and slower. Static RAM is used to create the CPU’s speed sensitive cache, while dynamic RAM forms the larger system RAM space.” [1]

## Slide 3
Table 1: Comparison between the SRAM and DRAM [2]
“SRAM | DRAM
SRAM has lower access time, so it is faster compared to DRAM. | DRAM has higher access time, so it is slower than SRAM.
SRAM is costlier than DRAM. | DRAM costs less compared to SRAM.
SRAM requires a constant power supply, which means this type of memory which consumes more power. | DRAM offers reduced power consumption because the information is stored in the capacitor.
It is a complex internal circuitry, and it offers less storage capacity is available compared to the same physical size of a DRAM memory chip. | It is the small internal circuitry in the one-bit memory cell of DRAM. The large storage capacity is available.
SRAM has a low packaging density. | DRAM has a high packaging density.”

## Slide 4: Other RAM Types:
1- Synchronous Dynamic Random Access Memory (SDRAM): “These RAM chips use the same clock rate as CPUuses. They transfer data when the CPU expects them to be ready.” [1]
2- Double Data Rate-Synchronous Dynamic Random Access Memory (DDR-SDRAM): “This RAM transfers data on both edges of the clock. Therefore the transfer rate of the data becomes doubles.” [1]

## Slide 5
RAM
SRAM
DRAM
DDR-SDRAM
SDRAM
DDR1
DDR4
DDR2
DDR3
Figure 1: Relationships between various RAM types

## Slide 6
Figure 2: Different RAMs of type Double Data Rate (DDR) [3]

## Slide 7: References:
[1] https://ecomputernotes.com/fundamental/input-output-and-memory/what-are-the-different-types-of-ram-explain-in-detail
[2] https://www.guru99.com/different-types-ram-random-access-memory.html?fbclid=IwAR38uXeJTm9i32v3zw09uw-b3amS4t9-M7XCZFYLiC7ckzU32rOS8rpFwp4
[3] https://techlog360.com/ddr1-ddr2-ddr3-ddr4-ram-differences/

## Slide 8: Wish You All the Best